## Slide 1
EIRSAT-1 ADCS
Daire Sherwin, Joseph Thompson, Victorio Ubeda
01/09/2017
The EIRSAT-1 project is carried out with the support of the Education Office of the European Space Agency, under the educational Fly your Satellite! Programme

## Slide 2: Software
MATLAB / Simulink
  Highly standardized in control engineering
  MATLAB integrates well with other simulation software
  Can generate C / C++ code
Level-2 S functions
  Allow the integration of custom Matlab code into Simulink

## Slide 3: ADCS Model
Dynamics
Orbital Dynamics
Rotational dynamics
Disturbances
Aerodynamic drag
Gravity gradient
Solar radiation
Internal magnetic Dipole
Environment
Magnetic Field
  (IGRF. Spherical harmonics)
Sensors
Delay
[…]
Mode selection
Detumbling
Zenith pointing
Sun pointing
Reference
Control
PID
LQR
WBC
Actuator
+
+

## Slide 4: Rotational Dynamics
Rotational Dynamics and Kinematics
  Dynamics.
    Euler Equations
  Kinematics
    Quaternions
      Why quaternions?
        Euler angles / Roll – Pitch – Yaw may produce singularities when calculating Rotation Matrix

## Slide 5: Orbital Dynamics
Short time Scale
No need for precision in position
  Assumed circular orbit
  Constant orbit angular velocity
  Specified Argument of Periapsis and True Anomaly

## Slide 6: Reference
Two reference quaternions
  Zenith / Nadir Pointing
  Sun Pointing (Inertial reference frame)
%% Picture of reference frames %%

## Slide 7: Wave – Based Control
Launch a Wave
Absorb the returning wave
Reject disturbances

## Slide 8: Wave – Based Control
Launch a Wave
Absorb the returning wave
Reject disturbances

## Slide 9: Mode selection
Detumbling
  […]
Zenith / Nadir Pointing
  […]
Sun pointing
  […]

## Slide 10: Sensors
Clyde Space Board
  Magnetometer
  IMU
  GPS
  Coarse Sun Sensor

## Slide 11: Sensors
Delay
  […]
Noise
  […]
State Estimation (?). Extended / Unscendent Kalman Filters

## Slide 12: Disturbances
Aerodynamic drag
Gravity gradient
Solar radiation
Internal magnetic Dipole

## Slide 13: Solver
Runge Kutta 4 / 6
Variable step
Handled automatically by Simulink

## Slide 14: Limitations and Improvements
Standardized Frame transformations
Full documentation
Third – Body Forces

## Slide 15: Hardware. Clyde Space Board
%% Technical specifications from manual %%

## Slide 16: Hardware. Clyde Space Board
%% Technical specifications from manual %%

## Slide 17: OrbSim: Overview
Set of C libraries, incorporating multiple standard packages, to carry out simulation, Python scripts for plotting and data analysis.
Features require a version of C no older than C99.
Developed on Windows using MinGW environment.
Intended to be compatible with different OS’s
  No use of multi-threading
  Shouldn’t require changes to path/environment variables

## Slide 18: OrbSim: Overview
Second-order Ordinary Differential Equation solver
  Runge-Kutta 6 for higher accuracy
  Runge-Kutta 4 available for more rapid testing
  Fixed time-step of 30s
Force model consists of
  Earth’s point mass gravitational field
  Spherical harmonic corrections (EGM08 model)
  Drag force (NRLMSISE-00 model)
  Sun, Moon third-body perturbations
  Solar Radiation Pressure
Satellite rotation modelled using quaternions

## Slide 19: OrbSim: Overview
Multiple custom structs
  Cartesian state vector
  Reference frame (Satellite-centered frame)
  Space-weather entry
  Satellite
Most ephemerides, frame transformations, coordinate conversions, etc. handled by the NAIF SPICE Toolkit
  Positions of other bodies in the Solar System
  Inertial (J2000), body-fixed (ITRF93) frame conversions
  Geodetic coordinates (latitude, longitude)
  Orbital Elements

## Slide 20: OrbSim: Issues
Built on code with very different focus
  Has required multiple iterations, currently on OrbSim v3.
Limitations to standard tools, SPICE in particular
  Transformation of acceleration vector
    Trial-and-error solution found
  Older version of SPICE missing some useful features
    Will be corrected in the future when there’s time
  Orbital elements known to be unsuitable for high-accuracy work
    Primary calculations done using Cartesian state vector
Inefficiency still an issue
  To be corrected in the future

## Slide 21: OrbSim: Current State
De-orbit prediction (w/o rotation)
within one day of ESA’s software
(345 days).
Satellite rotation accounted for
(zenith pointing for now) (280 days)

## Slide 22: OrbSim: Current State
Thermal Model generated
  Still some de-bugging required
  Minor issue with satellite
  rotation
Power generation from solar panels
  Still some de-bugging required
  Accurate figures from solar panel
  specs needed.

## Slide 23: OrbSim: Current State
Ground track
Orbital Elements

## Slide 24: Going Forward
Last major features to be added
  Radiation dosage
  Best/worst case scenarios for drag force
  Make initial setup easier and more user friendly
Fully comment code
Collate python scripts into one Post-Processing.py
Options and setup files, which will allow the user to run code on different scenarios without recompilation
Upload to Github
Continue to work on improving efficiency

## Slide 25: Going Forward
Many extra features which would be nice to have
  Adaptive step-size functionality for ODE solver
  Communications with ground station
  Expansion to non-elliptical orbits (can solve for them, but orbital elements conversion not well-defined)
  Error Analysis
  Addition of magnetic field effects to force model
  Generalize orientation calculation(s)
  Addition of operations
    Commands which would be passed to satellite in reality (eg. deployment of additional solar panels, re-orientation, etc.)
  Generalization to larger-scale missions?
    Orbital manoeuvres, launchers, etc.
  GUI?

## Slide 26: Going Forward
MASTER/DRAMA
  On-orbit collision risk assessment
  Re-entry risk assessment
    Will EIRSAT-1 burn up on re-entry?
    Does it pose a risk to human life?
  Accidental break-up risk
  Sanity check for results of OrbSim

## Slide 27
Thank you
Any Questions?