## Slide 1
EIRSAT-1 ADCS
(Attitude Determination and Control System)
Daire Sherwin, Joseph Thompson, Victorio Ubeda
01/09/2017
The EIRSAT-1 project is carried out with the support of the Education Office of the European Space Agency, under the educational Fly your Satellite! Programme

## Slide 2
Introduction
Model
  Theory
  Simulink
  Results
Hardware
%% Not to sure about this slide %%

## Slide 3: ADCS Simulations. Software
MATLAB / Simulink
  Highly standardized in control engineering
  MATLAB integrates well with other simulation software
  Can generate C / C++ code
Level-2 S functions
  Allow the integration of custom Matlab code into Simulink
Pros | Cons
Readily installed math libraries and toolboxes | ‘Black box’ compared to other programming languages
%% Beginning of presentation %%

## Slide 4: ADCS Simulations. Software
MATLAB / Simulink
  Highly standardized in control engineering
  MATLAB integrates well with other simulation software
  Can generate C / C++ code
Level-2 S functions
  Allow the integration of custom Matlab code into Simulink
Pros | Cons
Readily installed math libraries and toolboxes | ‘Black box’ compared to other programming languages

## Slide 5: ATTITUDE

## Slide 6: CONTROL
Dynamics
Reference
Control

## Slide 7: ATTITUDE CONTROL
+
Dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
Actuator
+
Ground Segment

## Slide 8: ATTITUDE CONTROL
+
Dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
Actuator
+
Ground Segment

## Slide 9: SENSORS
+
Dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
Actuator
+
Ground Segment

## Slide 10: SENSORS
Clyde Space ADCS Board
  Magnetometer
  IMU
  GPS
  Coarse Sun Sensor
Dynamic response
  Delay
  Noise
  Uncertainty
State Estimation.
  Kalman filters

## Slide 11: SENSORS
+
Dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
Actuator
+
Ground Segment

## Slide 12: Mode selection
Detumbling
Zenith / Nadir Pointing
Sun pointing (Inertial reference)
Animation Sun Pointing
Animation Zenith Pointing

## Slide 13: Environment. Magnetic field
Spherical harmonics approximation
  International geomagnetic reference (IGRF), provided by International
  Currently 12th generation
Plots

## Slide 14: Environment. Magnetic field
Spherical harmonics approximation
  International geomagnetic reference (IGRF), provided by International
  Currently 12th generation
Plots

## Slide 15: ADCS Model
+
Dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
Actuator
+
Ground Segment

## Slide 16: ADCS Model
+
Dynamics
Orbital Dynamics
Rotational dynamics
Sensors
Disturbances
Environment
Mode selection
Reference
Control
WBC
Actuator
+
Ground Segment

## Slide 17: ADCS Model
+
Dynamics
Orbital Dynamics
Rotational dynamics
Sensors
Delay
Noise
Errors
Disturbances
Aerodynamic drag
Gravity gradient
Solar radiation
Internal magnetic Dipole
Environment
Magnetic Field
  (IGRF. Spherical harmonics)
Mode selection
Detumbling
Zenith pointing
Sun pointing
Reference
Desired
Attitude
Control
PID
LQR
WBC
Actuator
MagneticTorquers
+
Ground Segment

## Slide 18: ADCS Model
+
Dynamics
Orbital Dynamics
Rotational dynamics
Disturbances
Aerodynamic drag
Gravity gradient
Solar radiation
Internal magnetic Dipole
Environment
Magnetic Field
  (IGRF. Spherical harmonics)
Sensors
Delay
Noise
Errors
Mode selection
Detumbling
Zenith pointing
Sun pointing
Reference
Desired
Attitude
Control
PID
LQR
WBC
Actuator
MagneticTorquers
+
Ground Segment

## Slide 19
%% Questions? %%
  Is the choice of this structure clear?
  Why this particular arrangement?

## Slide 20: Dynamics
Rotational Dynamics and Kinematics
  Dynamics.
    Euler Equations
  Kinematics
    Quaternions
    Euler angles / Roll – Pitch – Yaw may produce singularities when calculating Rotation Matrix
%% ... But not time %%
%% Choice of C.S. %%
%% 3D rotations complicated because…
%% Hamilton solved this…

## Slide 21: Dynamics
Rotational Dynamics and Kinematics
  Dynamics.
  Kinematics
    Quaternions
    Euler angles / Roll – Pitch – Yaw may produce singularities when calculating Rotation Matrix
Orbital Dynamics
  No need for precision in position
  Assumed circular orbit
    Constant orbit angular velocity
    Specified Argument of Periapsis and True Anomaly
Argument of periapsis and true anomaly

## Slide 22: Orbital Dynamics
Orbital Dynamics
  Short time Scale
  No need for precision in position
  Assumed circular orbit
    Constant orbit angular velocity
    Specified Argument of Periapsis and True Anomaly
%% Diagram %%
%% What I mean with this is that we do not
simulate translation accurately %%

## Slide 23: Reference
Two reference quaternions
  Zenith / Nadir Pointing
  Sun Pointing (Inertial reference frame)
Reference frames

## Slide 24: Wave – Based Control
Launch a Wave
Absorb the returning wave
Reject disturbances
%% WBC was developed originally at UCD by Dr William J. Oconnor %%

## Slide 25: Wave – Based Control
Launch a Wave
Absorb the returning wave
Reject disturbances

## Slide 26: Wave – Based Control
Developed originally at UCD by Dr. William J. O’connor
  No model needed
  Robust to system changes
  Robust to actuator limitations
  Stable, fast, smooth
  Computationally light

## Slide 27: Wave – Based Control
Two ESA contracts
  Delian Arm
  IXO

## Slide 28: Disturbances
Gravity gradient
  Neglectable for CubeSat size
Solar radiation pressure
Aerodynamic drag %% The biggest (?) one %%
Internal magnetic Dipole %% The biggest (?) one %%
%% Ussually, 4 tipes of disturbances are considered,
but for EIRSAT, two of them are much greater
than the others %%
Plot
Plot

## Slide 29: Actuators. Magnetorquers
Magnetic torquers
  No inverse for vector product
    Pseudo – inverse
    SR – inverse
    Projection of the control troque
  Scenarios
    Three ideal actuators
    Three magnetorquers
    Two magnetorquers
    One magnetorquer
%% Magnetic field, normal plane,
control torque, dipole,
actuator torque %%

## Slide 30: Solver
Runge Kutta 4 / 6
Variable step
Handled automatically by Simulink
%% Add some more %%

## Slide 31: Solver
Runge Kutta 4 / 6
Variable step
Handled automatically by Simulink

## Slide 32: Limitations and Improvements
Standardized coordinate systems and reference frames
  SPICE
Full documentation
  In process
Third – Body Forces
Sun reference

## Slide 33: Hardware. Clyde Space Board
%% Technical specifications from manual %%

## Slide 34: Hardware. Clyde Space Board
%% Technical specifications from manual %%

## Slide 35: Documentation

## Slide 36: References